## Slide 1
Starch Consumption Analysis — DS Smith PM1 Witzenhausen
Report Date: March 17, 2026
Analysis Period: March 3–17, 2026 (2 weeks)
Cutoff: March 12, 2026
Filter: Running periods only (reel speed > 100 m/min)

## Slide 2
Executive Summary
Starch consumption declined after March 12 across most product grades
4 of 7 comparable grades show 10–19% reduction in dry starch usage (t/h)
Pattern is consistent across grades → points to a process-level change, not just grade mix
Starch silo inventory dropped from ~290 t to a low of 118 t on March 16 before refill

## Slide 3
Overall Metrics (Running Periods Only)
Avg. dry starch rate — Before: 1.99 t/h | After: 2.08 t/h (+4.5%)
Avg. silo inventory — Before: 235 t | After: 210 t (−11%)
Note: Overall rate appears stable because high-consuming grade 6035135 ran heavily after March 12
Per-grade analysis reveals the true reduction pattern

## Slide 4
Per-Grade Comparison — Grades That Decreased
3200140: 2.06 → 1.68 t/h (−18.6%) — highest-volume grade, largest drop
6010120: 2.04 → 1.74 t/h (−14.6%)
3300130: 1.55 → 1.35 t/h (−12.8%)
6035135: 3.54 → 3.14 t/h (−11.4%) — highest absolute consumer
3200115: 1.72 → 1.67 t/h (−3.0%) — minor change

## Slide 5
Per-Grade Comparison — Grades That Increased
6010140: 1.87 → 2.16 t/h (+15.5%)
3300165: 2.07 → 2.24 t/h (+8.4%)
Possible causes: recipe adjustments or different operating conditions during those runs

## Slide 6
Grades Without Comparison
The following grades ran only before March 12 — no after-period data available:
3200155 — avg 2.69 t/h
3202170 — avg 2.87 t/h
3300185 — avg 1.87 t/h
6035150 — avg 3.53 t/h

## Slide 7
Silo Inventory Trend
March 12: ~290 t (full)
March 13–15: Steady decline as consumption continued without replenishment
March 16: Low point at ~118 t — potentially critical level
March 16–17: Refill delivery restored stock to ~249 t
Recommendation: Review delivery scheduling to prevent critically low inventory

## Slide 8
Key Findings
Consistent reduction across most grades indicates a process-level change around March 12
Possible drivers: starch recipe change, enzyme dosing adjustment, or SpeedSizer parameter change
Two grades (6010140, 3300165) showed increases — investigate separately
Grade mix shifted: several grades only produced before March 12
6035135 remains the highest starch consumer at 3.1–3.5 t/h in both periods

## Slide 9
Recommended Next Steps
1. Verify process changes — Check starch recipe, enzyme dosage, SpeedSizer settings around March 12
2. Quality validation — Cross-check Cobb, SCT, burst strength to confirm no quality impact
3. Silo replenishment — Improve delivery scheduling to avoid critical lows (118 t on March 16)
4. Standardize if beneficial — If quality is on-spec, lock in lower starch rates as new centerlining targets

## Slide 10
Data Sources & Methodology
F27700.IN — Dry starch flow rate (calculated), t/h
W27700.IN — Total starch silo inventory, t
S26791.IN — Master reel speed (running filter), m/min
Running threshold: > 100 m/min
Sampling resolution: 15 min
Production data: PM1 production runs matched by timestamp
Report generated by Juna Factory AI — March 17, 2026